## Slide 1: Active RDMA
Chris Fallin, Anshul Madan, Filipe Militão
15-712: Advanced Operating Systems & Distributed Systems

## Slide 2: Introduction & Motivation
Classic tradeoff in distributed systems:
  RPC style semantics:
    Static interface accessible through RPC calls
    Calls can be optimized
  Remote DMA style semantics:
    Increased flexibility by exposing data structures
    High separation of data and (running) code

## Slide 3: Propose & Prototype
A middle ground: Active RDMA
  Keep the flexibility of RDMA…
  … but enable data-code locality with code migration (active code).
client
server
code
Memory
NETWORK

## Slide 4: RDMA traffic
Operation: p->next->next->val
client
server
READ
READ
READ

## Slide 5: Active RDMA traffic
Operation: p->next->next->val
client
server
LOAD CODE
EXECUTE CODE
READ
READ
READ
(init)

## Slide 6: Contributions
Run active code directly on the NIC
  low-level interface for remote code
  reference implementation of Active RDMA
Simulation infrastructure:
  modified Bochs x86 + Java JVM + timing model
Initial evaluation of the concept:
  distributed (in-memory) FS vs NFS
  performance impact: grep + ﬁnd + copy

## Slide 7: Related Work
Active Networks
  customization at the network/routing level
Active Disks
  execute code at the disk controller
  mostly data processing
Mobile Code
  higher level abstraction
  sandboxing and security
Notes: - primarily proposed for customization at the network or routing layer
- more generic than active disks (any distributed system with shared state at the server).
- focus on performance benefits than mobile code (runs on the NIC).

## Slide 8: Active RDMA Architecture
client
server
Memory
code
code
NETWORK

## Slide 9: Active RDMA - primitives
Existing RDMA primitives like read, write, CAS
Our extensions:
  Load ( bytecode )
  Execute( md5, args )

## Slide 10: Initial Test Applications
Linked List
Locking Service
Hash table

## Slide 11: Active RDMA File System (ARFS)
Alloc
Inode+Data
ARFS Active Code
Memory
CLIENT
SERVER
ARFS Client
NETWORK
Hashtable
Hashtable
Inode+Data

## Slide 12: ARFS Architecture
Uses other Active code as libraries:
  Alloc()
  Hash table : Path  Address
  Inode store : Address  Data blocks
  FS interface :
    Hash table + Inode store
     hierarchical data store

## Slide 13: Evaluation Methodology
Active RDMA FS (ARFS) vs. NFS
ARFS-rdma, ARFS-active variants
Tests:
  Andrew Benchmark
  Stream-Read
  Stream-Write
Find, Grep:
  system utilities
  active versions

## Slide 14: Simulation
Bochs full-system simulator
JVM “coprocessor” in NIC model
UDP/IP stack in NIC model
Client: FUSE (userspace)
Benchmarks run on host
Wallclock time + synthetic timing statistics

## Slide 15: Basic Benchmarks

## Slide 16: Find and Grep

## Slide 17: CPU Load Scaling Behavior

## Slide 18: Packet Roundtrips

## Slide 19: Synthetic Runtime: RDMA vs. Active

## Slide 20: Future Work
Better methodology
  Acceptable but tractable: pace JVM appropriately, model network delay, run client in separate Bochs
  Better: Extend cycle-accurate simulated domain to clients and network, build cycle-accurate model of active code coprocessor (real ISA, cache coherence with main CPU, …)
  Best: prototype in a real system
    Active code (i) in server kernel or (ii) on real NIC (FPGA?)
    Clients with in-kernel filesystem

## Slide 21: Future Work II
Implementation: more robust (optimized IO path, robust error handling, …)
Server-side architecture:
  Sync with main host CPU (at least for on-disk FS)
  consider tradeoffs between coprocessor and main processor
Dynamic active code generation
  Grep: regex compiler? (after basic optimizations)
  More complex data queries, custom adapters, …

## Slide 22: Summary & Conclusion
Designed Active RDMA interface and presented reference implementation
Built proof-of-concept in-memory network filesystem
Evaluated performance in simulation
Showed a few active code-specific applications
Lessons learned:
  Getting API right is hard (underwent a few changes)
  Define basic services, build in layers
  Getting accurate simulation/timing for client/server setups is HARD
Underwhelming prototype performance, but interesting possibilities for future